## Slide 1
Figure X. Data Flagging Decision Tree
Both of these questions must be true for “Yes”:
1.) Are one or both samples above LOQ?
2.) Are one or both samples at least 2x LOQ?
Field Sample Value
[DRAFT] Kenai Watershed Forum Agency Baseline Water Quality Project
Relative Percent Difference (RPD) Data Flagging Flowchart
Duplicate Sample Value
Yes
No
Calculate RPD Value
Do Not Calculate RPD Value
Is the RPD value below QAPP goals?
Yes
No
Submit values for this parameter to EPA WQX Database
Examine fieldwork notes for explanation; justify decisions to flag data or not for this parameter
Unique Parameter & Sampling Event on Single Day
Duplicate Samples at Two Locations
Are both values below LOQ?
Yes
No
Submit values for this parameter to EPA WQX Database [???]
Unclear [???]
LOQ – Limit of Quantitation
RPD – Relative Percent Difference
QAPP – Quality Assurance Project Plan